## Slide 1
SCHOOL OF COMPUTING AND INFORMATION TECHNOLOGY
An Investigation Hardware design for portable ECG monitoring using Machine Learning
Presented By:
Md Kaif Mustafa (R21EJ020)
Rahul Kumar Singh (R21EJ026)
Major Project Phase-II
Under the Supervision
Dr. Syed Thouheed Ahmed
1

## Slide 2: Overview
Introduction
Abstract
Literature Survey
Research Gap
Problem Statement
Methodology
Deliverables
References

## Slide 3: Introduction
01
An Electrocardiogram (ECG) is a medical test that detects heart problems by measuring the electrical activity generated by the heart as it contracts.
The signals are measured using electrodes attached to the skin.
The portable ECG machine proposed in this project is aimed at creating a small, battery-powered ECG that can be easily carried for monitoring and recording heart signals.
This device is particularly suitable for rural areas, where access to large medical equipment is limited.

## Slide 4: Abstract
02
The portable ECG machine project aims to create a compact, cost-effective, and reliable device for capturing heart activity signals.
This project utilizes an AD8232 ECG sensor module and an Arduino Nano to process and transmit data wirelessly using a Bluetooth module.
The objective is to design a user-friendly ECG machine suitable for home monitoring and telemedicine purposes.
This document outlines the complete hardware setup, component details, cost estimation, and possible future enhancements.
This project investigates the design and development of a portable Electrocardiogram (ECG) monitoring device that leverages Machine Learning (ML) to enhance real-time heart health diagnostics

## Slide 5: Literature Survey
03
[1]ECGs are essential for the diagnosis of heart conditions, their expensive cost prevents them from being widely available in developing nations. In order to increase accuracy and lower noise in portable systems, research emphasises the use of AgCl electrodes, analogue circuits, and signal processing approaches. Replication, cost, and web-based monitoring for scalability are the main areas of focus. In order to improve accessibility in environments with limited resources, this study suggests a portable, inexpensive ECG machine that combines these developments.
[2]Due to restricted access to healthcare, heart disease is more common in rural areas. This is addressed by IoT-based ECG systems, which make predictive analysis, cloud data transmission, and real-time monitoring possible. In order to enhance accessibility and diagnoses in underprivileged areas, this study suggests a smart ECG system.

## Slide 6
04
High data rates and power consumption in [3] are problems for portable ECG systems. VPW-FRI and IF-TEM are two examples of sub-Nyquist sampling techniques that provide effective, asynchronous, and power-efficient solutions. In order to achieve precise heart rate monitoring, this work creates an IF-TEM-based ECG sampling technique with strong filters for noise resistance, which is verified by hardware implementation.
[4]Cardiovascular diseases are the leading cause of death globally, with abnormal heart signals as key indicators. Existing ECG devices lack portability and rely on manual data analysis, limiting efficiency. Recent studies have applied machine learning, combining traditional models like SVM and XGBoost with deep learning models like CNNs and LSTMs, to improve ECG classification.
The integration of AI in [5], particularly deep learning (DL) models, has significantly advanced ECG signal analysis and arrhythmia detection. Models like CNNs, LSTMs, and hybrid architectures (e.g., CNN-AE and CNN-SVM) have achieved high accuracy, outperforming cardiologists in some cases.

## Slide 7
05
[6]ECG equipment are essential for identifying cardiac issues, low-income groups frequently cannot afford them. In order to save costs, this study suggests a portable, inexpensive ECG device that uses an Arduino Uno microcontroller. The system is widely usable since it provides wireless connectivity for data transfer to PCs and smartphones. It was discovered that the designed machine's ECG reading accuracy had acceptable error margins and was on par with commercial ECG devices.
The necessity for accessible in [7], reasonably priced healthcare solutions is underscored by the rising incidence of sudden cardiac arrest in emerging nations. Cost-effective cardiac monitoring devices that record critical data including BPM, ECG, and SpO2 have been developed using IoT technology. With real-time data transfer to a smartphone app via a Raspberry Pi3b+, this system improves emergency response by providing immediate notifications.
[8]To avoid cardiac arrest, ECG abnormalities must be detected early. This paper suggests a portable ECG gadget that uses a Raspberry Pi to interpret real-time data collected by an ECG sensor. To identify the commencement of an arrhythmia, the collected characteristics are subjected to Discrete Wavelet Transform (DWT) analysis and then classified using a trained SVM algorithm. By using real-time monitoring and anomaly detection, the system seeks to facilitate timely medical intervention.

## Slide 8
06
This study in [9] presents a real-time ECG signal acquisition system based on the TMS320VC5509A DSP chip. The system captures and processes ECG signals through analog filtering, amplification, and digital conversion, followed by low-pass filtering in the DSP for display on an LCD. It offers advantages such as compact size, low power consumption, low cost, and real-time processing.
[10] Paper presents a portable ECG recorder combining a signal amplifier, ADC, and USB storage for easy ECG measurement and data transfer. It allows real-time monitoring and heart rate calculation using the R-wave peak. The system offers a convenient, portable solution for ECG recording and analysis.

## Slide 9: Research Gap
07
Lack of Accessible and Affordable Cardiac Monitoring
Current Issue: Traditional ECG machines are bulky, expensive, and require a clinical setting, which limits regular cardiac monitoring for patients in remote or under-resourced areas.
Research Gap: There is a need for a cost-effective, portable ECG system that enables continuous monitoring outside of hospitals, making heart health tracking more accessible for home users and rural populations.
Integration of Real-Time Data Acquisition with Wireless Communication
Current Issue: While several portable ECG solutions exist, many either lack real-time data visualization or do not support wireless data transmission for remote monitoring.

## Slide 10
Research Gap: Your project fills the gap by integrating real-time ECG waveform capture with Bluetooth-enabled wireless data transmission, allowing immediate access to heart activity on smart devices.
User-Friendly and Scalable Telemedicine Solutions
Current Issue: Existing systems often have limited user interfaces and do not offer comprehensive data management or future scalability.
Research Gap: By incorporating a web application (with features like patient data input, data export, and alert notifications) alongside the hardware, your project creates an end-to-end solution. This not only simplifies user interaction but also lays the foundation for future enhancements like mobile app integration and cloud storage.
Holistic Approach to System Design
Current Issue: Many previous studies have focused on isolated aspects of portable ECG systems—such as improving signal acquisition or reducing power consumption—without offering a complete, integrated solution.
08

## Slide 11
Research Gap: Your project bridges this divide by addressing hardware design (using AD8232, Arduino Nano, and Bluetooth module), software implementation (signal processing and visualization), and potential for advanced analytics (e.g., AI-based signal processing). This comprehensive approach meets the need for an all-in-one, scalable monitoring system.
09

## Slide 12: Problem Statement
Conventional ECG machines are bulky, expensive, and limited to clinical settings, which restricts timely cardiac monitoring for patients—especially those in remote or under-resourced areas. This limited access delays early detection of heart abnormalities and ongoing management of cardiac health. Therefore, there is a critical need for a low-cost, portable ECG solution that reliably captures heart signals and wirelessly transmits real-time data for continuous monitoring and telemedicine applications.
This statement captures the key issues: the high cost and inaccessibility of traditional ECG systems, the impact on patient care, and the necessity for an innovative solution.
10

## Slide 13: Methodology
This chapter outlines the methodology adopted for the development of the Portable ECG Machine. The methodology encompasses the selection of components, circuit design, software implementation, data acquisition, processing, and transmission. The approach ensures that the device is reliable, cost-effective, and user-friendly, making it suitable for home and remote healthcare applications.
Hardware Methodology
Component Selection
The selection of components is critical to the accuracy and efficiency of the ECG machine. The following components were chosen based on their performance and compatibility:
AD8232 ECG Sensor Module – Captures heart signals with built-in amplification and filtering.
Arduino Nano – A compact microcontroller for processing the ECG signals.
HC-06 Bluetooth Module – Enables wireless data transmission to external devices.
Electrodes – High-quality Ag/AgCl electrodes ensure reliable signal acquisition.
Rechargeable Battery Pack – Provides portability and prolonged operation.
11

## Slide 14
Circuit Design and Setup
The circuit is designed to facilitate efficient data acquisition, processing, and transmission. The key connections include:
The AD8232 module is connected to the Arduino Nano via analog input pins.
The Bluetooth module (HC-06) is interfaced with the Arduino Nano via serial communication (TX/RX pins).
A 5V power supply is used to power all components, ensuring stable operation.
Electrodes are placed on the user’s body to detect heart signals, which are then fed into the AD8232 for initial processing.
Software Methodology
Data Acquisition and Processing
The ECG signal is acquired using the AD8232 sensor and sent as an analog input to the Arduino Nano. The Arduino utilizes the analogRead() function to capture real-time data. The signal undergoes further processing, including:
Filtering: Basic low-pass and high-pass filters remove noise and artifacts.
Amplification: The built-in amplifier in the AD8232 module enhances weak ECG signals.
12

## Slide 15
Digitization: The analog ECG waveform is converted into digital data for transmission.
Wireless Data Transmission
To facilitate real-time monitoring, the processed ECG data is transmitted wirelessly via the HC-06 Bluetooth module. The Arduino communicates with the Bluetooth module using serial communication, and the data is transmitted using the Serial.print() function.
User Interface and Visualization
The transmitted ECG data can be received on a smartphone, tablet, or PC using a compatible application. The data is displayed as a real-time ECG waveform, allowing users to monitor their heart activity. Future enhancements may include mobile app integration for improved data analysis and storage.
System Testing and Validation
To ensure the reliability and accuracy of the device, the following testing procedures are performed:
Signal Accuracy Testing: Comparing ECG waveforms generated by the device with standard ECG machines.
13

## Slide 16
Noise Reduction Analysis: Evaluating the effectiveness of filtering techniques in minimizing signal distortions.
Wireless Connectivity Testing: Assessing the range and stability of Bluetooth data transmission.
User Experience Evaluation: Gathering feedback from potential users to refine the device’s design and interface.
Model Selection and Training Train a machine learning model, such as a convolutional neural network (CNN) or support vector machine (SVM), on a dataset of ECG signals to classify normal and abnormal rhythms (e.g., arrhythmias).
Model Optimization for Embedded Systems Optimize the trained model for deployment on the microcontroller by using techniques like model quantization, pruning, or converting it to a TensorFlow Lite or TinyML format. This ensures the model runs efficiently with limited computational resources.
Embedded ML Integration Program the optimized model into the microcontroller to analyze ECG data in real-time and detect anomalies. Configure the system to trigger alerts when abnormal patterns are detected.
14

## Slide 17: Deliverables
Hardware Prototype
Fully assembled and functional Portable ECG Machine
Integration of AD8232 ECG Sensor Module, Arduino Nano, and Bluetooth Module
Rechargeable battery pack for portability
Circuit Design and Schematics
Circuit diagram showing all electrical connections
Block diagram outlining the working of the ECG system
15

## Slide 18
Software Implementation
Arduino Code for data acquisition, processing, and Bluetooth transmission
Mobile/PC interface (App or Software) for real-time ECG visualization
Data storage (PDF/CSV) for record-keeping
Testing and Validation Reports
Signal Accuracy Comparison with standard ECG machines
Noise Filtering Efficiency analysis
Bluetooth Connectivity Testing results
Power Consumption and Battery Performance evaluation
16

## Slide 19
Future Enhancements Plan
Mobile App Integration for better user experience
Cloud Storage and Remote Access for advanced monitoring
AI-based Signal Processing for abnormality detection
Bluetooth/Wi-Fi Communication Setup Configure the wireless module for seamless communication between the device and a mobile application or cloud storage.
Mobile App Development Develop a mobile application to display real-time heart rate data, ECG visualizations, and alert notifications. Include secure data storage and encryption protocols for user privacy.
Remote Monitoring Integration Enable options for data storage on the cloud to allow users and healthcare providers to monitor long- term cardiac health trends remotely
17

## Slide 20: References
[1] Rakin, Rafaeal & Siam, Asad & Hossain, Md & Zaman, Hasan. (2019). A Low-Cost and Portable Electrocardiogram (ECG) Machine for Preventing Diagnosis. 48-53. 10.1109/ICREST.2019.8644425.
[2] Nagdive, Arundhati. (2024). Portable ECG Machine with Future Prediction. International Journal for Research in Applied Science and Engineering Technology. 12. 96-101. 10.22214/ijraset.2024.59705.
[3] Naaman, Hila & Bilik, Daniel & Savariego, Shlomi & Namer, Moshe & Eldar, Yonina. (2024). ECG-TEM: Time-based sub-Nyquist sampling for ECG signal reconstruction and Hardware Prototype. 10.48550/arXiv.2405.13904.
18

## Slide 21
[4] Su, Shi & Zhu, Zhihong & Wan, Shu & Sheng, Fangqing & Xiong, Tianyi & Shen, Shanshan & Hou, Yu & Liu, Cuihong & Li, Yijin & Sun, Xiaolin & Huang, Jie. (2023). An ECG Signal Acquisition and Analysis System Based on Machine Learning with Model Fusion. Sensors. 23. 1-21. 10.3390/s23177643.
[5] Lichaee, Fatemeh & Salari, Arsalan & Jalili, Jalil & Dalivand, Sedigheh & Rad, Mahdis & Mojarad, Mohadeseh. (2024). Advancements in Artificial Intelligence for ECG Signal Analysis and Arrhythmia Detection: A Review. International Journal of Cardiovascular Practice. 8. 10.5812/intjcardiovascpract-143437.
[6] Muhibul Haque Bhuyan , Md. T. Hasan, Hasan Iskander, Low-Cost Microcontroller Based ECG Machine, Vol:14, No:7, 2020
19

## Slide 22
[7]Stepheny Lucas, Mitali Desai, Amisha Khot, Sincee Harriet, Kavita Jain, Mobile Heart Sync: An IoT Based Portable ECG Monitor, 10.56155/978-81-955020-7-3-27
[8] Niyatha Malepati, Rubia Fatima, Swarnima Gupta ,Vaishnavi Ramsali, Shobha K.R. , Portable ECG Device for Remote Monitoring and Detection of Onset of Arrhythmia, 10.1109/CONECCT50063.2020.9198658
[9] Khushi Singh, Malaya Kumar Hota , Design and development of DSP enabled low- cost ECG machine , 10.1109/ICEEICT53079.2022.9768423
[10] C. S. Ho, T. K. Chiang, C. H. Lin, P. Y. Lin, J. L. Cheng, S. H. Ho, Design of Portable ECG Recorder with USB Storage, 10.1109/EDSSC.2007.4450319
20

## Slide 23
Thank You